## Slide 1
Literature Survey
ECE4500j
- Title: Replacing a cloud-based computation tool on DrBoxOnline.com with faster running neural network
- Team Members: Yanzhuo Cao, Fengyu Zhang, Keye Chen, Shuo Deng, Yukuan Zhu
- Section Instructor: Jigang Wu
- Project Sponsor: Shane Johnson
Notes: Hello everyone, we are team 15, and the title of our project is Replacing a cloud-based computation tool on DrBoxOnline.com with faster running neural network.

## Slide 2
Background
Issue: Corrosion in pipelines causes significant safety and maintenance challenges.
Limitations: Traditional methods (e.g., ASME B31G) are conservative, leading to excessive maintenance.
Achievements
FEM: High precision but computationally intensive.
ANN: Fast and accurate with sufficient training data.
Methodology
Integration: Combining FEM and ANN for better efficiency and accuracy.
Experiments: Using FEM-generated data to train ANN models.
Future Directions
Optimization: Improve FEM-ANN frameworks for more accurate predictions.
Applications: Validate models with real-world data for broader use.
Keywords: Failure pressure, FEM, ANN Search Engine: Google Scholar
Paper 1 [1]
Notes: Now I will introduce the first paper named "A Review of Finite Element Analysis and Artificial Neural Networks as Failure Pressure Prediction Tools for Corroded Pipelines," addresses pipeline corrosion issues. Traditional methods like ASME B31G are conservative, leading to excessive maintenance.
FEM is precise but slow, while ANN offers fast, accurate predictions with enough training data. The study suggests combining FEM and ANN to enhance efficiency and accuracy. Experiments using FEM data to train ANN models showed promising results.
Future directions include optimizing these frameworks and validating them with real-world data. This integration aims to improve safety and reduce costs in pipeline maintenance.

## Slide 3
Background
Issue: Predicting mechanical properties is crucial for engineering applications.
Limitations: Traditional experimental methods are time-consuming and costly.
Achievements
Machine Learning: Effective for predicting various material properties
Deep Learning: Extracts complex patterns from data, improving prediction accuracy.
Methodology
ML Techniques: Support Vector Machines, k-Nearest Neighbors, Decision Trees.
DL Techniques: Convolutional Neural Networks, Recurrent Neural Networks.
Future Directions
Optimization: Enhance AI models for better accuracy and efficiency.
Applications: Expand AI methods to more complex and diverse composite materials.
Keywords: Machine Learning, Mechanical Property Search Engine: Google Scholar
Paper 2 [2]
Notes: The second paper, "Artificial Intelligence in Predicting Mechanical Properties of Composite Materials," tackles the challenge of predicting mechanical properties. Traditional experimental methods are time-consuming and costly.
Machine Learning (ML) techniques, such as Support Vector Machines, k-Nearest Neighbors, and Decision Trees, have proven effective. Deep Learning (DL) techniques, including Convolutional Neural Networks and Recurrent Neural Networks, extract complex patterns from data, improving prediction accuracy.
The paper highlights the potential of ML and DL in predicting material properties more efficiently and accurately. Future directions focus on enhancing AI models for better accuracy and expanding their application to more complex composite materials.

## Slide 4
Background
Issue: Solving forward and inverse nonlinear problems described by partial differential equations (PDEs) using data that is often noisy.
Limitations: Previous models, like physics-informed neural networks (PINNs), struggled with overfitting and were inadequate in scenarios involving significant noise, lacking robust uncertainty quantification.
Achievements
Developed Bayesian Physics-Informed Neural Networks (B-PINNs) that offer more accurate predictions and effective uncertainty quantification in noisy environments.
Methodology
Experiments: Conducted systematic comparisons between HMC and VI for B-PINNs and evaluated the effectiveness of dropout for uncertainty quantification in deep neural networks.
Future Directions or Limitations
Optimization: While the integration of a truncated Karhunen-Loève (KL) expansion showed speed and accuracy, it’s limited by its inapplicability to high-dimensional problems, suggesting a potential area for future enhancement.
Keywords: Bayesian Physics-Informed Neural Networks Search Engine: Google Scholar
Paper 3 [3]

## Slide 5
Background
Issue: The DMD process, while efficient for producing complex parts, induces significant residual stresses and distortions, complicating the manufacturing of precise components.
Limitations: Existing methods for evaluating residual stress distributions are extensive and labor-intensive, involving a considerable amount of modeling and experimental work.
Achievements
Developed a novel artificial neural network-based modeling approach, integrated with finite element analysis, that significantly improves the accuracy and efficiency of predicting residual stresses in parts produced by DMD.
Methodology
Integration: The new methodology combines artificial neural networks with finite element analysis to overcome the shortcomings of traditional thermo-mechanical finite element models.
Experiments: Evaluated the performance of the new model on parts made of AISI 304L, focusing on different geometrical structures to assess the predictive accuracy and computational improvements.
Future Directions or Limitations
Optimization: The approach needs further development to be universally applicable across different materials and more complex geometrical configurations, which could extend its utility in industrial applications.
Keywords: Direct Metal Deposition(DMD). Search Engine: Google Scholar
Paper 4 [4]

## Slide 6
[1] Vijaya Kumar SD, Lo Yin Kai M, Arumugam T, Karuppanan S. A Review of Finite Element Analysis and Artificial Neural Networks as Failure Pressure Prediction Tools for Corroded Pipelines. Materials. 2021; 14(20):6135. https://doi.org/10.3390/ma14206135
[2] Kibrete F, Trzepieciński T, Gebremedhen HS, Woldemichael DE. Artificial Intelligence in Predicting Mechanical Properties of Composite Materials. Journal of Composites Science. 2023; 7(9):364. https://doi.org/10.3390/jcs7090364
[3] Yang, L., Meng, X., & Karniadakis, G. E. (2021). B-PINNs: Bayesian physics-informed neural networks for forward and inverse PDE problems with noisy data. Journal of Computational Physics, 425, 109913. https://doi.org/10.1016/j.jcp.2020.109913
[4] Hajializadeh, F., & Ince, A. (2021). Integration of artificial neural network with finite element analysis for residual stress prediction of direct metal deposition process. Materials Today Communications, 27, 102197. https://doi.org/10.1016/j.mtcomm.2021.102197
References

## Slide 7
Thanks for Listening!
Notes: 我的分享就到这里，谢谢大家！